## Slide 1: EC 614: Adaptive Signal Processing Techniques Course Instructor: Dr. Debashis Ghosh
Department of Electronics & Computer Engg.
Indian Institute of Technology Roorkee

## Slide 2: Syllabus
Definitions, assumptions and requirements of adaptive signal processing applicable to different application examples; Linear filter structures; Adaptive beamforming (4 lectures).
Optimum linear combiner and Wiener-Hopf equations, orthogonality principle, minimum mean square error and error performance surface; Multiple linear regression model; Linearly constrained minimum-variance filter (6 lectures).

## Slide 3: Syllabus (contd.)
Forward and backward prediction error filters; Levinson—Durbin algorithm; Properties of prediction-error filters; Autoregressive modeling of a stationary stochastic process; All-pole, all-pass lattice filter (8 lectures).
Steepest-descent algorithm and its stability; Principles of stochastic gradient descent, LMS algorithm and its variants (4 lectures).
Least Squares method, its efficient implementation: Minimum sum of error squares, normal equations and linear least-squares filters, Singular value decomposition, cyclic Jacobi, Householder methods (8 lectures).

## Slide 4: Syllabus (contd.)
RLS adaptive filtering algorithms; Exponentially weighted RLS algorithm; Kalman filter and its variants; Square-root adaptive filters, adaptive beamforming (8 lectures).
Implementation examples: Adaptive modeling and system identification, inverse adaptive modeling, equalization and deconvolution, adaptive control systems, adaptive interference cancellation (4 lectures).

## Slide 5: Suggested Texts / References
S. Haykin, “Adaptive Filter Theory”, Pearson Education.
B. Widrow and S.D. Stearns, “Adaptive Signal Processing”, Pearson Education.
D.G. Manolakis, V.K. Ingle and M.S. Kogon, “Statistical and Adaptive Signal Processing”, Artech House.
H. Sayed Ali, “Fundamentals of Adaptive Filtering”, Wiley-Interscience, IEEE Press.
H. Sayeed Ali, “Adaptive Filters”, 1st Edn., John Wiley & Sons.
P.S.R. Diniz, “Adaptive Filtering: Algorithms and Practical Implementation”, Springer.

## Slide 6: Basics
Problem: Equalise through an FIR filter the distorting effect of a communication channel that may be changing with time.
If the channel were fixed then a possible solution could be based on the Wiener filter approach
We need to know in such case the correlation matrix of the transmitted signal and the cross correlation vector between the input and desired response.
When the filter is operating in an unknown environment these required quantities need to be found from the accumulated data.
The problem is particularly acute when not only the environment is changing but also the data involved are non-stationary

## Slide 7: Basics
In such cases we need temporally to follow the behaviour of the signals, and adapt the correlation parameters as the environment is changing.
This would essentially produce a temporally adaptive filter.
Algorithm

## Slide 8: Applications of Adaptive DSP
Digital communications
Channel equalization
Adaptive noise cancellation
Adaptive echo cancellation
System identification
Smart antenna systems
Blind system equalization
And many, many others

## Slide 9: Application: Channel Equalization

## Slide 10: Example: Weiner Filter
FIR filter tap weights can be found using the Weiner-Hopf equation: Rwopt = p
  where correlation matrix R = E [ x(n) xH(n) ] and cross-correlation vector p = E [ x(n) d*(n) ]
Based on the minimization of the mean-square error J(n) = E [ e(n) e*(n) ] where e(n) = d(n) – wH.x(n)
For changing signal statistics and/or channel condition, the filter weights are required to be updated continuously over time.

## Slide 11: Example: Weiner Filter
One approach may be using steepest-descent method.
We will study later that the weight updation may be done as
δw(n) = w(n+1) – w(n)
= μ [ p – Rw(n) ]
= μ E [ x(n)d*(n) – x(n)xH(n)w(n) ]
= μ E [ x(n) { d*(n) –xH(n)w(n) } ]
= μ E [ x(n) e*(n) ]

## Slide 12: Application: Noise Cancellation
Noise
Signal +Noise
-
+
FIR filter
Adaptive Algorithm
PRIMARY SIGNAL
REFERENCE SIGNAL

## Slide 13: Application: Echo Cancellation
-
+
-
+
Rx1
Rx2
Tx1
Tx2
Echo canceller
Echo canceller
Adaptive Algorithm
Adaptive Algorithm
Hybrid
Hybrid
Local Loop

## Slide 14: Application: System Identification
Unknown System
Signal
-
+
FIR filter
Adaptive Algorithm

## Slide 15: Application: Blind Equalization
Unknown System
Signal
-
+
FIR filter
Adaptive Algorithm
Delay

## Slide 16: Application: Adaptive Predictors
Signal
-
+
FIR filter
Adaptive Algorithm
Delay

## Slide 17: Application: Smart antenna arrays
Linear Combiner
Interference

## Slide 18: Algorithm for adaptation
Basic principles:
  Form an objective function (performance criterion)
  Find gradient of objective function with respect to FIR filter weights
  There are several different approaches that can be used at this point, e.g. steepest-descent method.
  Form a differential / difference equation from the gradient.

## Slide 19: Adaptive Filters
An adaptive filter is in reality a nonlinear device, in the sense that it does not obey the principle of superposition.
Adaptive filters are commonly classified as:
  Linear
    An adaptive filter is said to be linear if the estimate of quantity of interest is computed adaptively (at the output of the filter) as a linear combination of the available set of observations applied to the filter input.
  Nonlinear
    Neural Networks

## Slide 20: Linear Filter Structures
The operation of a linear adaptive filtering algorithm involves two basic processes:
  a filtering process designed to produce an output in response to a sequence of input data
  an adaptive process, the purpose of which is to provide mechanism for the adaptive control of an adjustable set of parameters used in the filtering process.
These two processes work interactively with each other.

## Slide 21: Linear Filter Structures
The impulse response of a linear filter determines the memory order of the filter:
  Infinite impulse response (IIR) filter
  Finite impulse response (FIR) filter
There are three types of filter structures with finite memory :
  transversal filter,
  lattice predictor,
  and systolic array.

## Slide 22: Transversal or Tapped Delay Line Filter

## Slide 23: Lattice Predictor
It has the advantage of simplifying the computation

## Slide 24: Systolic Array
Represents a parallel computing network ideally suited for mapping a number of linear algebra computations, e.g. matrix multiplication, triangularization, back substitution, etc.
Two basic processing elements:
(a) Boundary cell and (b) Internal cell

## Slide 25: Triangular Systolic Array
The use of systolic arrays has made it possible to achieve very high throughput, which is required for many advanced signal processing algorithms to operate in real time

## Slide 26: The three basic forms of estimation
The function of receiver is to operate on the received signal and deliver a reliable estimate of the original message.
Filters may be used for the purpose of estimation using one of the following three information-processing operations.
  Filtering
  Smoothing

## Slide 27: The three basic forms of estimation
  Prediction
Given an optimality criterion we can design optimal filters
  Requires a priori information about the environment
  Example: Under certain conditions the so called Wiener filter is optimal in the mean-squared sense
Adaptive filters are self-designing using a recursive algorithm
  Useful if complete knowledge of environment is not available a priori.

## Slide 28: Linear Filters
For stationary inputs, the resulting solution is commonly known as the Wiener filter, which is said to be optimum in the mean-square sense.
A plot of the mean-square value of the error signal vs. the adjustable parameters of a linear filter is referred to as the error-performance surface.
The minimum point of this surface represents the Wiener solution.

## Slide 29: Linear Filters
The Wiener filter is inadequate for dealing with situations in which non-stationarity of the signal and/or noise is intrinsic to the problem.
A highly successful solution to this more difficult problem is found in the Kalman filter, a powerful device with a wide variety of engineering applications.

## Slide 30: Linear Adaptive Filtering Algorithms
Stochastic Gradient Approach
  Least-Mean-Square (LMS) algorithm
  Gradient Adaptive Lattice (GAL) algorithm
Notes: An introductory discussion of linear adaptive filters would be incomplete without saying something about their tracking behavior. In this context, we note that stochastic gradient algorithms such as the LMS algorithm are model independent; generally speaking, we would expect them to exhibit good tracking behavior, which indeed they do. In contrast, RLS algorithms are model dependent; this, in turn, means that their tracking behavior may be inferior to that of a member of the stochastic gradient family, unless care is taken to minimize the mismatch between the mathematical model on which they are based and the underlying physical process responsible for generating the input data.

## Slide 31: Linear Adaptive Filtering Algorithms
Least-Squares Estimation
  Recursive least-squares (RLS) estimation
    Standard RLS algorithm
    Square-root RLS algorithms
    Fast RLS algorithms
Notes: An introductory discussion of linear adaptive filters would be incomplete without saying something about their tracking behavior. In this context, we note that stochastic gradient algorithms such as the LMS algorithm are model independent; generally speaking, we would expect them to exhibit good tracking behavior, which indeed they do. In contrast, RLS algorithms are model dependent; this, in turn, means that their tracking behavior may be inferior to that of a member of the stochastic gradient family, unless care is taken to minimize the mismatch between the mathematical model on which they are based and the underlying physical process responsible for generating the input data.

## Slide 32: Stochastic Gradient Approach
Most commonly used type of Adaptive Filters
Define cost function as mean-squared error
    Difference between filter output and desired response
Based on the method of steepest descent
  Move towards the minimum on the error surface to get to minimum
  Requires the gradient of the error surface to be known

## Slide 33: Least-Mean-Square (LMS) Algorithm
Most popular adaptation algorithm is LMS
  Derived from steepest descent
  Doesn’t require gradient to be known: it is estimated at every iteration
Consists of two basic processes
  Filtering process
    Calculate the output of FIR filter by convolving input and taps
    Calculate estimation error by comparing the output to desired signal

## Slide 34: Least-Mean-Square (LMS) Algorithm
  Adaptation process
    Adjust tap weights based on the estimation error

## Slide 35: Four classes of applications
Used to provide a linear model of an unknown plant
Applications:
  System identification

## Slide 36: Four classes of applications
Used to provide an inverse model of an unknown plant
Applications:
  Equalization

## Slide 37: Four classes of applications
Used to provide a prediction of the present value of a random signal
Applications:
  Linear predictive coding

## Slide 38: Four classes of applications
Used to cancel unknown interference from a primary signal
Applications:
  Echo cancellation

## Slide 39: Beamforming
Smart Antenna systems:
  Switched beam: finite number of fixed predefined patterns
  Adaptive array: Infinite number of (real time) adjustable patterns

## Slide 40: Beamforming
Adaptive filtering: An array of independent sensors placed at different locations in space essentially samples the received signal spatially.
Applications: Radar, Sonar, Speech enhancement, etc.
Smart Antenna systems: Using a variety of new signal-processing algorithms, the adaptive system takes advantage of its ability to effectively locate and track various types of signals to dynamically minimize interference and maximize intended signal reception.

## Slide 41: Beamforming
Beamforming: spatial filtering
  The sensor outputs are individually weighted and then summed to produce overall beamformer output.
The term derived from the fact that early antennas were designed to form a pencil like beam so as to receive signal radiating from a specific direction and to attenuate signals originating from other directions that are of no interest.
Beamforming applies to both transmission as well as reception.

## Slide 42: Beamforming: Uniform line array
x0(t)
d
x1(t)
x2(t)
xM(t)
s(t)
(M-1)



## Slide 43: Beamforming: Delay-sum
Timed array
+
(t-[M-1]T)
(t-[M-2]T)
(t)
w0
x
w1
x
wM-1
x

## Slide 44: Beamforming: Delay-sum

## Slide 45: Beamforming: Narrowband phased array
x0[n]
+
x
x
x
x1[n]
xM-1[n]
We may eliminate time delays and use complex weights, w = [w0, …, wM-1]T, to both steer (phase align) and weight (control beam shape)

## Slide 46: Beamforming: Similar to FIR filter
Tapped delay line
+
x
x
x
Represent signal delay across array as a delay line
Sample: x[n] = x0(nT) = s(nT)
y[n] = x[n]*w[n]
Looks like an FIR filter.
Design w with FIR methods so as to maximize the output
(t-)
(t-)
y(t)
x[n]

## Slide 47: Beamforming: Narrowband
Narrowband assumption: If BW of s(t) << c / (M-1)d Hz.
This means the phase difference between upper and lower band edges for propagation across the entire array is small.
Most communication signals fit this model.
Check that d must be less than half-wavelength (λ/2); this ensures one-to-one correspondence between θ (lying in the range [−π/2, +π/2] ) and ξ (lying in the range [−π, +π] ).
If signal is not narrowband, bandpass filter it and build a new beamformer for each subband.

## Slide 48: Beamforming

## Slide 49: Beamforming

## Slide 50: Beamforming
An optimal weight vector satisfying our requirement is of the form
Amplitude components control the sidelobe level and main beam width.
m = amplitude weight for sensor m,
mξ = phase weight for sensor m,
f0 = bandpass center frequency, 0 = direction of max response

## Slide 51: Beamforming

## Slide 52: Beamforming
Thus, we define beamforming as
  Beam forming is a method used to create the radiation pattern of an array antenna by adding constructively the weights of the signals in the direction of SOI and nulling the pattern in the direction of SNOI (interference)
This array can be antennas in the smart antennas context, or any other types of sensors (radars, medical sensors, …, etc), can be an array of microphones in the speech signal processing context.

## Slide 53: Beamforming
Beamforming can be used at both the transmitting and receiving ends in order to achieve spatial selectivity
That is, an appropriate feeding allows antenna arrays to steer their beam and nulls towards certain directions, this is often referred to as spatial filtering.

## Slide 54: Beamforming

## Slide 55: Factors for choice of filter / algorithm
Choice of Adaptive filters:
  Computational cost
  Performance
  Robustness
Choice of recursive algorithm:
  Rate of convergence
  Misadjustment
  Tracking

## Slide 56: Factors for choice of filter / algorithm
  Robustness
  Computational requirements
  Structure
  Numerical properties