## Slide 1: Wiener Filters Course Instructor: Dr. Debashis Ghosh
Department of Electronics & Computer Engg.
Indian Institute of Technology Roorkee

## Slide 2: Syllabus
Optimum linear combiner and Wiener-Hopf equations, orthogonality principle, minimum mean square error and error performance surface; Multiple linear regression model; Linearly constrained minimum-variance filter (6 lectures).

## Slide 3: Introduction
The process of extracting the information-carrying signal s[n] from the observed signal x[n] = s[n] + η[n], where η[n] is a noise process, is called filtering.
Typical filters are designed based on a frequency response approach
Wiener filters, on the other hand, are based on a statistical approach.
x[n]
s[n]
η[n]
h[n]

## Slide 4: Introduction
The Wiener filter was proposed by Norbert Wiener in 1940 and was published in 1949.
Its purpose is to reduce the amount of a noise in a signal.
This is done by comparing the received signal with a estimation of a desired noiseless signal.
Wiener filter is not an adaptive filter as it assumes input to be stationery.

## Slide 5: Introduction
Goal of the filter is to remove the noise from a signal such that the resultant signal required is as close to the original signal.
Wiener filter takes a statistical approach to solve its goal.
If the spectral properties of the signals involved are known, an LTI filter can be designed whose output would be as close as possible to the original signal.
The aim of the process is to have minimum mean- square error. That is, the difference between the original signal and the new signal should be as less as possible.

## Slide 6: Statement of the problem
To filter a signal x[n] so as to modify it such that it approximates some other signal d[n] in some statistical sense.
That is, the output of the filter y[n] is a good estimate of the desired response d[n].
The output error e[n] represents the mismatch between y[n] and d[n], i.e. estimation error.

## Slide 7: Some assumptions
x[n] is wide-sense stationary, i.e. it has constant (and finite) mean and variance, and a correlation function which is a function of time shift only:
A stronger condition would be to assume that x[n] is strong-sense stationary, i.e. all of its moments are constant and finite.
An even stronger condition would be to assume that x[n] is ergodic, i.e. all of its sample averages converge to the true moments.
These latter two conditions are presently not necessary.

## Slide 8: Some assumptions
All of the signals are zero-mean.
In order to talk about an “optimal” filter which estimates d[n] from x[n], we must have a method of measuring how good a job the filter does.
A “cost function” or “error criterion” is used to judge the performance, and could take on many different forms.
In Wiener filter, MSE (mean square error) is taken as the cost function (error criterion):
J

## Slide 9: Some assumptions
Other cost functions that may be used:
  Expectation of absolute value of the estimation error.
  Expectation of third or higher powers of the absolute value of the estimation error.
However, advantages of using MSE are:
  2nd order dependence of the cost function on the unknown coefficients of the filter impulse response  mathematically tractable.
  Cost function has a distinct minimum that uniquely defines the optimum statistical design of the filter.

## Slide 10: Some assumptions
Restrictions on the filter:
  Linear: mathematical analysis easy to handle.
  Discrete-time: possible to implement using digital hardware and/or software.
  FIR: inherently stable and easy to handle when the filter is required to be adaptive (since it does not involve feedback path)

## Slide 11: Principle of orthogonality

## Slide 12: Some mathematical notes
The gradient is a fancy word for derivative, or the rate of change of a function.
It is a vector (a direction to move) that
  Points in the direction of greatest increase of a function
  Is zero at a local maximum or local minimum (because there is no single direction of increase)
The term "gradient" is typically used for functions with several inputs and a single output (a scalar field).

## Slide 13: Some mathematical notes

## Slide 14: Some mathematical notes
Complex derivative: If a function is continuous at a point z = x + jy, we then can define its complex derivative as
In principle, we might get different results from the above formula when we plug in different infinitesimals δz, even in the limit where δz → 0 and even though f(z) is continuous.

## Slide 15: Some mathematical notes
To cope with this complication, we regard the complex derivative as well-deﬁned only if the above deﬁnition gives the same answer regardless of the argument of δz.
If a function f(z) satisﬁes this property at a point z, then we say that the function is complex-diﬀerentiable at z.
In other words, a complex-diﬀerentiable function is one possessing an unambiguous complex derivative.
If a function f(z) is complex-diﬀerentiable for all points z in some domain D ⊂ ₵, then f(z) is said to be analytic (or holomorphic) in D

## Slide 16: Some mathematical notes

## Slide 17: Some mathematical notes

## Slide 18: Principle of orthogonality

## Slide 19: Principle of orthogonality (contd.)

## Slide 20: Principle of orthogonality

## Slide 21: Wiener-Hopf eqautions

## Slide 22: Wiener-Hopf equations

## Slide 23: Wiener-Hopf eqautions
These equations give the required optimum filter coefficients (weights).
These equations are called Weiner-Hopf equations.
For FIR filter with finite M number of filter taps, the Weiner-Hopf equations reduce to a system of M number of simultaneous equations.

## Slide 24: Minimum MSE

## Slide 25: Minimum MSE

## Slide 26: Error performance surface
Cost function

## Slide 27: Error performance surface
J is a 2nd order function of the filter tap-weights
(M+1)-dimensional bowl-shaped surface with M degrees of freedom
Jmin attained at the bottom of the bowl.
At this point

## Slide 28: Error performance surface
This means,
This also leads to the same Wiener-Hopf equations.
So, condition for min. MSE is
This leads to principle of orthogonality and the Wiener-Hopf equations follow from there.
In a second approach, express cost-function J directly in terms of filter tap-weights, find the gradients, equate to zero to get the same Wiener-Hopf equations.

## Slide 29: Matrix formulation of the W-H equations
This may be written as
is correlation matrix (covariance matrix for zero mean) of the tap-input vector , is the required optimum tap-weight vector and p is the cross-correlation vector.
Input vector

## Slide 30: Matrix formulation of the W-H equations
Check that r[−k] = r*[k]
It follows

## Slide 31: Matrix formulation of MMSE
Or,
Note that =
Therefore,
=

## Slide 32: Matrix formulation of error surface